## Slide 1: McStas Union components
Mads Bertelsen, ESS DMSC

## Slide 2: Multiple scattering
Multiple scattering can happen in all systems
Adding several materials complicates matters
In spatially large systems time of flight is affected by multiple scattering

## Slide 3: Multiple scattering
t = s lambda
k_f
k_i
q
q_1
q_2
k_f
k_i
q
q_1
q_2
k_f
k_i
q
q_1
q_2
Multiple scattering can happen in all systems
Adding several materials complicates matters
In spatially large systems time of flight is affected by multiple scattering

## Slide 4: Concentric keyword in McStas
Simple sample container
COMPONENT a = Container_1(concentric=1, …) AT (0,0,0) RELATIVE sample_position
COMPONENT b = Sample(…) AT (0,0,0) RELATIVE sample_positon
COMPONENT c = Container_2(concentric=0,…) AT (0,0,0) RELATIVE Container_1

## Slide 5: Concentric keyword in McStas
Sample environment
COMPONENT a = Container_1(concentric=1, …) AT (0,0,0) RELATIVE sample_position
COMPONENT b = Sample(…) AT (0,0,0) RELATIVE sample_positon
COMPONENT c = Container_2(concentric=0,…) AT (0,0,0) RELATIVE Container_1

## Slide 6: Union introduction
Modular geometry and physics
Aims to simulate complex systems
All trajectories allowed

## Slide 7: Union overview
Geometry
Materials
Processes

## Slide 8: Union process syntax
COMPONENT Al_incoherent = Incoherent_process( sigma=4*0.0082,packing_factor=1, unit_cell_volume=66.4) AT (0,0,0) ABSOLUTE
COMPONENT Al_powder = Powder_process( reflections="Al.laz") AT (0,0,0) ABSOLUTE
COMPONENT Al = Union_make_material( my_absorption=100*4*0.231/66.4, process_string=“Al_incoherent,Al_powder”) AT (0,0,0) ABSOLUTE
my [1/m] = cross section per unit cell / unit cell volume

## Slide 9: Union concepts: Priority
Vanadium priority = 5.1
Priority to handle overlapping geometries
The highest priority is simulated in regions where more are overlapping
Aluminium priority = 8.2

## Slide 10: Union concepts: Priority
Priority to handle overlapping geometries
The highest priority is simulated in regions where more are overlapping

## Slide 11: Union concepts: Syntax
COMPONENT cryostat_shell = Union_cylinder( radius=0.15,height=0.4, priority=10,material_string="Al") AT (0,0,0) RELATIVE target ROTATED (0,0,0) RELATIVE target
COMPONENT cryostat_vacuum = Union_cylinder( radius=0.147,height=0.39, priority=11,material_string="Vacuum") AT (0,0,0) RELATIVE target ROTATED (0,0,0) RELATIVE target

## Slide 12: Union concepts: Syntax
COMPONENT cryostat_shell = Union_cylinder( radius=0.15,height=0.4, priority=10,material_string="Al") AT (0,0,0) RELATIVE target ROTATED (0,0,0) RELATIVE target
COMPONENT cryostat_vacuum = Union_cylinder( radius=0.147,height=0.39, priority=11,material_string="Vacuum") AT (0,0,0) RELATIVE target ROTATED (0,0,0) RELATIVE target
COMPONENT cryostat = Union_master() AT (0,0,0) RELATIVE target ROTATED (0,0,0) RELATIVE target

## Slide 13: Union concepts: Syntax

## Slide 14: Union concepts: Syntax
Define process
Define material (many processes)
Define geometries (one material each)
Define loggers (optional)
Define conditionals (on loggers)
Execute simulation (defined geometries)
Issue: tangent planes / points

## Slide 15: Exercise
File with a number of material definitions, source, Union sample and monitors
Expand to include some sample environment!