## Slide 1: Single crystals and powders
Practical:

## Slide 2: Agenda
Laue Camera
  Build along in 4 steps!
Use the diffractometer
  PSI_DMC
Laue Camera revisited

## Slide 3: Build along Laue Camera
First insert a source
File → New Instrument
Insert → Sources → Source_simple
// insert components here (e.g. Insert -> Source -> ...)
COMPONENT source_simple = Source_simple(
radius=0.05,
dist=5,
focus_xw=0.02,
focus_yh=0.05,
lambda0=2,
dlambda=1.9)
AT (0, 0, 0) RELATIVE PREVIOUS

## Slide 4: Build along Laue Camera
Now add a guide
Insert → Optics → Guide
COMPONENT guide = Guide(
w1=0.02, h1=0.05, w2=0.02, h2=0.05, l=20, m=1)
AT(0,0,2) RELATIVE source_simple

## Slide 5: Build along Laue Camera
Add a sample – in this case a standard crystal
Insert → Samples → Single_crystal
COMPONENT single_crystal = Single_crystal(
reflections="Al2O3_sapphire.lau",
yheight=0.05, radius=0.01, mosaic=1, delta_d_d=1e-4,
az=4.757, ay=0, az=0, bx=2.3785, by=0, bz=-3.364,
cx=0, cy=12.9877, cz=0,
p_transmit=0.1)
AT (0, 0, 0) RELATIVE PREVIOUS

## Slide 6: Build along Laue Camera
Add the ideal Laue Camera Monitor – covering 4π
Insert → Monitors → PSD_monitor_4PI
COMPONENT fourpi = PSD_monitor_4PI(
radius=1, filename="fourpi.dat", nx=201, ny=201)
AT(0,0,0) RELATIVE PREVIOUS

## Slide 7: Build along Laue Camera
Run your simulation (you can safely increase the number of rays to 10^7) the ncount) – you should get something like:
Press L for
logarithmic

## Slide 8: Build along Laue Camera
Play around with this example instrument:
Add an Arm components before the sample to allow rotation around the Y-axis.
Add “SPLIT 20” before the sample COMPONENT statement. What happens?
Try to extend this to Y, Z, Y rotation (Eulerian cradle).
Insert a different crystal instead e.g. “Al.lau”. i.e. change the crystal unit cell parameters and the reflection list.
Insert a powder sample instead

## Slide 9
PowderN exercise
In this exercise we will try to put two powder samples together in a few ways and compare the results.
Two samples in the same spot, and stochastically choose between them
Two samples stacked vertically
Two samples where one is behind the other.

## Slide 10
PowderN exercise
Let’s use the PSI_DMC instrument as a starting point. We will now make the simulation randomly choose between two powders.
Add another powder in the same spot as the one already there.
Add double r; inside the DECLARE section of the instrument file.
Add an Arm in front of the first one, and add to it an EXTEND-block. Add the following code in it: r=rand01();
Now add the following before the AT on the two powders. WHEN(r<0.5) and WHEN(r>0.5) respectively.
Run the instrument again – Do you get what you expect?
What would you change to make the mixing factor !=0.5?

## Slide 11
PowderN exercise
Let’s change this to have two samples on top of each other.
Make a new copy of the instrument (or remove the edits you did before, leaving the second Powder sample in place).
Change the y-position and size of the samples to be +- height/2.0 and height/2.0 respectively
Add the statement GROUP sample after the AT at both samples. (N.b. sample is a name chosen arbitrarily. It has to be different than the component names though.)
Run a simulation – is there any difference to the previous result? Why/Why not?

## Slide 12
PowderN exercise
Move samples around such that one is in front of the other.
Run a simulation – Do you still see the signatures of both samples?
Do you remember why this can be?
How can we get around this?

## Slide 13
Intermission: A quick trick to remove the direct beam
If your monitor also can be hit by the direct beam, “swamping” the signal, you can do this:
Add the following code just after your sample code: EXTEND %{ if (!SCATTERED){ABSORB;}
%}
This will terminate all rays which the sample-code has not flagged as scattered. Bear in mind the McStas definition of scattered includes many things (guide-wall reflections etc.)

## Slide 14: Real Instruments
PSI DMC
Increase the height of the detector and make it resolve the signal along y.
Set:
Options="banana, theta y auto limits bins=20", yheight=0.3
In the detector.
...and change the sample to be e.g. an Aluminium crystal.
COMPONENT single_crystal = Single_crystal(
reflections="Al.lau",
yheight=0.05, radius=0.01, mosaic=1, delta_d_d=1e-4,
az=4.0495, ay=0, ax=0, bx=4.0495, by=0, bz=0,
cx=0, cy=4.0495, cz=0,
p_transmit=0.1)
AT (0, 0, 0) RELATIVE PREVIOUS